## Slide 1
Team WATT Pankaj Singh
K. Nithesh Kumar
Ram Prasad
Prisca Jean
Disaster-Resilient Shelter Management System Smart Disaster Shelter Entry & Capacity Monitoring System
Domain: Embedded Systems | IoT | Disaster Management

## Slide 2
Initial Problem Understanding
During disasters:
  Internet & cellular networks may fail
  Shelters get overcrowded
  Manual counting becomes unreliable
Volunteers lack real-time capacity awareness
Feedback from Previous Review
Avoid over-complex sensing
Focus on robustness, not perfect accuracy
Consider real-world noise & false detections
PROBLEM REFINEMENT

## Slide 3
Earlier Approach (Discarded)
Estimating:
  People sitting
  Standing
  Sleeping under beds
Sensing inside the shelter
Problems Identified
Need sensors on each bed
Or rotating sensors using servo motors
People sitting at:
  Different corners
  Different angles
Apparent length & occlusion issues
Becomes research-heavy & impractical
EARLIER IDEA & WHY WE DROPPED IT

## Slide 4
Shelter Entrance-Based Detection
Count people entering, not occupancy
One sensing point → entrance
Maintain shelter capacity state
Communicate wirelessly using LoRa
Why Entrance Detection?
FINAL REFINED IDEA
Single controlled point
No ambiguity of sitting/standing
No need for bed-level sensors
Easier to scale & deploy

## Slide 5
Sensors Considered
PIR Motion Sensor
IR Sensor
Ultrasonic Sensor
Load Cell (Weight sensor)
Real-World Challenges Identified
SENSOR SELECTION & DIFFICULTIES
PIR can falsely trigger due to:
  Birds / animals
  Sudden temperature changes
IR alone:
  Detects objects, not humans
Ultrasonic:
  Can misread reflections
Load cell:
  Can detect weight but not intent

## Slide 6
Role of PIR Sensor
Crowded shelters → uniform temperature
No thermal gradient
Stationary people → no PIR trigger
Why PIR Works at Entrance
WHY PIR IS STILL IMPORTANT
Continuous movement
Strong thermal contrast
People don’t wait long outside during disasters
Why PIR Failed Earlier (Inside Shelter)
Detects living motion (thermal change)
Helps reject:
  Bags
  Static objects
Acts as life-detection evidence

## Slide 7
Why Error Management is Needed
Sensors may:
  Give fake readings
  Temporarily fail
  Trigger due to noise
Confidence-Based Detection
SENSOR FUSION & ERROR MANAGEMENT
Each sensor contributes evidence, not a final decision.
Evidence | Score
PIR motion | +1
Weight detected | +1
Dynamic weight change | +1
Decision Rule
Confidence ≥ 2 → Valid human
Confidence = 1 → Rejected

## Slide 8
Handled Scenarios
PIR = YES
Weight = NO
Confidence = 1 → ❌ Rejected
FALSE DETECTION CASES (EXPLICIT)
🐦 Bird / Animal
🎒 Bag placed
Weight = YES (static)
PIR = NO
No dynamic change
Confidence = 1 → ❌ Rejected
PIR + Weight + Dynamic change
Confidence ≥ 2 → ✅ Count++
🚶 Human Entry
⚠️ Sensor Failure
PIR fails → Weight + dynamic works
Load cell fails → PIR + persistence works

## Slide 9
What We Count
People entering
NOT bed occupancy
NOT people sitting/sleeping
Logic
ENTRY COUNTING LOGIC
Each validated entry:
  peopleCount++
  Data sent via LoRa
3-second lockout
  Prevents double counting
  Handles lingering at entrance

## Slide 10
Why FSM?
Capacity States (Demo = 6)
FSM (FINITE STATE MACHINE)
Count | State
0 | EMPTY
1–2 | LOW
3 | HALF
4–5 | THREE_QUARTER
6 | FULL
Behavior When FULL
Stop counting
Send LoRa warning every second
Prevent overcrowding
Predictable behavior
Easy to explain
Review-friendly

## Slide 11
Shelter Node
Arduino UNO (or Nano)
Sensors
LoRa
2S 18650 battery
HQ Node
SYSTEM ARCHITECTURE
Arduino Nano
LoRa
USB → Laptop
Serial Monitor display
Shelter Node ~~~LoRa~~~> HQ Node → Laptop

## Slide 12
Why Arduino for Now
Already available
Simple & stable
Sufficient for logic & FSM
Lower power complexity
ESP32 as Future Scope
MICROCONTROLLER DECISION
Faster processing
Deep sleep capability
Sensor-triggered wake-up

## Slide 13
Challenges Faced
Sensor false positives
PIR limitations in crowded areas
Power regulation decisions
Over-engineering risk
How We Addressed Them
CHALLENGES & PITFALLS
Sensor fusion
Entrance-only detection
FSM-based logic
Simple, explainable architecture

## Slide 14
Project Timeline
23 Feb – Component procurement
Next week – Hardware assembly
Weekend (Sat–Sun) – Software integration
After 29–30 Feb – Final tuning & validation
Before 5 March – Final demo & review prep
TIMELINE